## Slide 1: Refining NOx Emissions using Satellite Observations Inverse Modeling through DART–CHIMERE Data Assimilation of S5P/TROPOMI NO2 Retrievals
25.06.2026 | CHIMERE Workshop
Giorgia De Moliner, Gaëlle Dufour, Gaël Descombes, Alessandro D'Ausilio, Adriana Coman, Guillaume Siour, Arineh Cholakian, Giovanni Lonati

## Slide 2: Motivations & context
01

## Slide 3: Why is refining emission fluxes needed?
Significant inter-product variability
Emission inventory uncertainties propagate into air quality simulations, degrading their skills
Bottom-Up Inventories
Since the availability of satellites measuring NO2 in the atmosphere, methods aligning a-priori inventories with observations have been developed (Streets et al., 2013)
Satellite-based top-down emissions provide a NRT constraint to detect unreported sources, capture rapid activity shifts, and address systematic biases in a-priori inventories
Top-Down Advantage
We tested the skill of the Ensemble Adjustment Kalman Filter (EAKF) CHIMERE-DART to perform Inverse Modeling for NOx, following Hsu et al. (2024), Savas et al. (2023) and Miyazaki et al. (2017)
CHIMERE-DART was developed within the EU’s project CAMEO (Descombes et al. (2026))
Ensemble-Based Inverse Modeling
Annual Emissions Fluxes (CAMS-REG-ANT v6.1)
Land Use Map
Vertical Distributions
Spatial Proxies
Temporal Allocation
Chemical Speciation
Emission Factors
Activity Data
Mapping of Sources
Hourly Emissions Fluxes
emiSURF v2023
Notes: Flux-Divergence
Plume Fitting
Mass Balance

## Slide 4: Data Assimilation
It is the process of optimally estimating the state of a dynamical system by combing observational data with an a priori estimate of the state
Key goal: constraining simulations with real-world observations
Z
X
Y
Chemical Transport Model
(CTM)
Observations
(Figure: A. Carrassi et al., 2018)
Ensemble Adjustment Kalman filter (EAKF)
(J. L. Anderson, 2001, 2009)
0
2
N
1
produce chemically/dynamically consistent integrated dataset
Knowledge of uncertenties
Mismatches between modelled and observed variables
Fast reactions and short lifetime of some species
The advantage of Ensemble Kalman filter (EnKF) is its easy implementa on for complicated systems; i.e., without development of adjoint code for CTMs.
Notes: The advantage of Ensemble Kalman filter (EnKF) is its easy implementation for complicated systems; i.e., without development of adjoint code for CTMs.
At its core, DA relies on the Bayes’ theorem, which provides the principle for updating the prior distribution. A practical way to solve the Bayesian estimation problem is given by the Kalman filter (KF). In this approach, the model is integrated forward in time and, whenever observations become available, they are used to update the prior before the integration continues. This sequential filtering process ensures that observations and model simulations are consistently combined to produce the best possible estimate of the true state of the atmosphere.
The following is a general description of the Kalman filter, as in Houtekamer and Mitchell, 2005 []. A prior estimate of the variable state xf(t), also called the background, valid at time t is updated with the information of the new observations yo to get a new estimate of the variable state xa(t), the analysis, as in Eq. (1). To this end, a Kalman gain matrix K is used to weight the observations and the background, according to their associated errors, represented by the observation error covariance matrix R and the background error covariance matrix Pf, respectively. The formulation of the Kalman gain is given in Eq. (2). In KFs, the background errors covariances are dynamically updated at each cycle, accounting for flow-dependency. The forward operator H performs the mapping of the estimates from the model space to the observation space, through a spatio-temporal interpolation and the use of averaging kernels. It computes model estimates as they would have been seen by the satellite, enabling a comparison between the model and the observations. Lastly, a forecast model M integrates the analysis xa(t) to the next variable state prior estimate xf(t+1) as in Eq. (3).
The KF analysis xa t is the best (minimum error variance) linear unbiased estimate of the state at time t, given xb t and all observations up to time t (y0,y1,…,yt).
In large systems, computing and storing the background errors covariances is impractical due to memory and computational constraints, as it would require running the model as many times as the dimension of state space. To overcome this, the ensemble Kalman filter (EnKF) [] and other ensemble-based methods were proposed. They all use Monte Carlo methods to reduce the problem dimension and to estimate the error covariances of the background error. In particular, EnKFs approximate Pf from an ensemble of model realizations, each having differently perturbated inputs.
Unlike variational approaches (3D-VAR (Kalnay, 2002), 4D-VAR (Courtier et al., 1994)), the EnKF method avoids the need for adjoint models and instead represents forecast uncertainty through an ensemble of simulations (Houtekamer & Zhang, 2016). Each member of the ensemble evolves independently under model dynamics with stochastic perturbations that represent model errors. The ensemble statistics provide a flow-dependent approximation of the forecast error covariance, allowing the analysis to converge toward the optimal Kalman solution as the ensemble size increases (Mitchell et al., 2002).

## Slide 5: EU’s space missions targeting atmospheric composition
Satellite | Instrument | Mission objectives | Spatial Resolution | Launch (operational) / EOL | Orbit | Provider | Reference
Sentinel-5P | TROPOMI (UV-VIS-NIR-SWIR) | O3, CO, HCHO, NO2, SO2, CH4, tot Aerosols and Clouds | 3.5 x 5 km | 2017 (2018) / ≥ 2027 | LEO, sun-synchronous, 1 day revisit time | ESA | https://space.oscar.wmo.int/instruments/view/tropomi https://sentiwiki.copernicus.eu/web/s5p-mission https://stcorp.github.io/harp/doc/html/ingestions/index.html#sentinel-5p-products
Metop-SG-A1 | Sentinel-5(A) (UV-VIS-NIR-SWIR) | O3, CO, CO2, H2O, HCHO, NO2, SO2, CH4, OCHCHO, BrO | 7 km | 2025 (2026) / 2034 | LEO, sun-synchronous, 1 day revisit time | EUMETSAT, ESA | https://user.eumetsat.int/resources/user-guides/metop-sg-sentinel-5-uvns-l1b-data-guide https://www.esa.int/Applications/Observing_the_Earth/Copernicus/Sentinel-5/Sentinel-5_debuts_images_of_atmospheric_gases
Meteosat-TG-S1 | Sentinel-4 (UV-VIS-NIR) | BrO, HCHO, NO2, O3, SO2, Aerosols and Clouds | 8 km | 2025 (2026) / 2036 | GEO, Europe, 1 hour revisit time | ESA, EUMETSAT | https://space.oscar.wmo.int/instruments/view/sentinel_4 https://www.eumetsat.int/first-copernicus-sentinel-4-images-showcase-europes-hourly-air-pollution-watch
Metop-(A)/B/C | GOME-2 (UV-VIS-NIR) | BrO, CHOCHO, H2O, HCHO, NO2, O2, O3, O4, OClO, SO2 and aerosol | 80 x 40 km | 2007 / 2033 | LEO, sun-synchronous, 1.5/3 days revisit time | ESA, EUMETSAT | https://space.oscar.wmo.int/instruments/view/gome_2 https://doi.org/10.5194/essd-15-1831-2023
Others: CO2M (0.8 km); TANGO (0.3/0.2 km)
WMO OSCAR tool
https://space.oscar.wmo.int/gapanalyses?variable=105
Notes: TEMPO, GEMS, OMI (nasa), Satellite NOAA-2, ISS-SAGE, OMS on Feng-Yun satellites
(more on GHGs: EMI and AIUS on GaoFen, TANSAT-2)
MetopSG-A1: has also IASI-NG and 3MI

## Slide 6: Methodology
02

## Slide 7: Workflow CHIMERE-DART
Observation
BCs (CAMS)
CTM-simulated observation
Ensemble CHIMERE runs
METEO (ECMWF)
Hourly Emissions Fluxes
Perturbations
EAKF
Refined NO2 ICs
Analysis
Refined
Hourly Emissions Fluxes
NO2 VCD
Annual Emissions Fluxes (CAMS-REG-ANT v6.1)
emiSURF v2023
Model space
Observation space
Forward Operator
NO2 & NO Emi Fluxes
NO2 Conc
Updated NO2 Conc
Updated NO2 & NO Emi Fluxes
DART
Forward Operator H
Fed through the ratio:
(Anderson, J. 2009)
NO2 & NO Emi Fluxes
NO2 Conc
State vector augmentation
Notes: observation operator that maps from the model state vector to the expected value of observations.
In (25), Dxm, n is the increment for ensemble member n of state vector component m, while sxm, y is the prior sample covariance of state vector component m and y. The term sxm, y/sp 2 in (25) is the form that the Kalman gain takes in the sequential EAKF. Figure 2 illustrates this part of the sequential EAKF algorithm.
The sample variance sp 2 of the prior estimate of the expected ‘observed’ model variables (observation) are computed

## Slide 8: LogNormal perturbations
The ensemble of prior emissions is generated by applying a spatially and temporally correlated noise to the given prior emission field, following previous studies as Coman et al. (2012), Barre et al.(2015), Gaubert et al. (2020), Deng et al. (2022).
α = magnitute of lognormal perturbations
β = index of temporal persistence
σ =spatial smoothing (as grid points)
= original emission flux
x = distance from center grid
 Perturbations drive model error estimation
        perturbated emission
        linear regression (AR1)
        pseudo-random white noise
        spatial Gaussian kernel
        white noise

## Slide 9: Prior emission ensemble

## Slide 10: Case study characteristics
Execution time
~1 h per simulated day on IRENE’s 22 CPU
CHIMERE-DART | 
Model | Chimere v2023 CTM (Menut. et al., 2024)
Domain & Resolutions | Continental Europe; 0.5°x0.5°; 20 levels
A Priori Emissions Dataset | CAMS-REG-ANT v6.1 (released: 2023) + emiSURF v2023r1 (Temporal profiles: Menut et al. 2012)
Meteo & Chemical BCs | ECMWF global reanalysis; CAMS regional reanalysis
Ensemble Size | 15 members
Perturbation Technique | Spatio-temporally correlated lognormal perturbation with zero mean
Assimilation Scheme & Tool | Ensemble Adjustment Kalman Filter (EAKF, J. Anderson et al., 2009); DART (Gharamti et al., 2025)
State Vector | NO2 concentration, NO2 & NO emissions
Observations | Superobbed-to-model-grid TROPOMI/S5P tropospheric vertical column of NO2 (QA>0.5)
Case test period | February 2020
Assimilation Techniques | Horizontal Localization (Gaspari-Cohn, half-width=120 km)
Assimilation Window | 1 hour (centered at the end of the CTM simulation)

## Slide 11: Results
03
Notes: Add take home messages

## Slide 12: Observation space Single overpass
2020-02-06 13:00 UTC
The analysis moves towards the observations and the spread is reduced

## Slide 13: Observation space 10-day average
2020-02-06 / 15
The analysis moves towards the observations and the spread is reduced

## Slide 14: Emissions correction Time evolution of analysis/prior NOx surface flux ratios
2020-02-06
Emission corrections reach high levels locally, averaging around 1.1 and 1.2 as orbit means
Ratio
Notes: slide 14: the timeseries of the ratio, is it the mean for all the domain or only chen you have the ratio different from 1?

## Slide 15: Emissions correction Surface NOx 10-day average emission relative increment (analysis – prior)/prior [%]
On average, inventories underestimate emission fluxes by 25% in this time period, with areas of largest corrections being the Po valley (Italy) as well as the harbours

## Slide 16: Comparison with control run Surface NO2 10-day average concentration change
Corrections introduced by cycling ICs and emission ratios to better match satellite observations have induced Chimere simulations to both increase and reduce NO2 surface concentrations
Control Run [%]

## Slide 17: Comparison with EEA monitoring stations Surface NO2 hourly concentration (subdomain’s stations averages)
Only background rural stations were selected
The gain of correcting emissions in a DA system is limited by the chosen emission update scheme
Notes: Others statistics decrease but very few

## Slide 18: Conclusions
03

## Slide 19: Conclusions and future work
We built and tested an emission inversion system on DART-CHIMERE, using a February 2020 case study to constrain NOx emissions using NO2 observations
Rather than replacing traditional bottom-up inventories, this system provides a dynamic constraint that identifies systematic biases and highlights priority regions for inventory refinement
First results are promising, emission correction are significant but a more extensive application is needed to assess the system’s general behavior
(Current and) future work will focus on investigating the role of model perturbations, assimilation settings (e.g. inflation, vertical localization) as well as improving the design of the emission update scheme between consecutive satellite overpasses

## Slide 20
Giorgia De Moliner
PhD student
giorgia.demoliner@polimi.it
Thank you
25.06.2026 | CHIMERE Workshop
Giorgia De Moliner, Gaëlle Dufour, Gaël Descombes, Alessandro D'Ausilio, Adriana Coman, Guillaume Siour, Arineh Cholakian, Giovanni Lonati
Notes: While the approach does not aim to replace established bottom-up inventories, the results indicate that satellite-informed emission corrections can provide additional, dynamically consistent constraints, supporting their use as a complementary component in CTM-based air quality analyses.

## Slide 21: Surface stations (timeseries, timeseries modelbias and gaelle figure)
Diff of avg
Model negative bias reduced by 6.8% in the cyIC case and by 8% in the cyIcEMISdmp. A +1.4% of hourly mean bias is achived by adding IM