## Slide 1
Challenges in modeling organic aerosols: comparing CHIMERE CTM results with measurements and PMF
Victor LANNUQUE, F. Couvidat (INERIS)
With special thanks to B. Murphy, H. Fagerli, D. Simpson (MetNO)
CHIMERE Workshop 2026
Paris, 25-26 June 2026

## Slide 2
Total OA Measurements (ACSM)
Organic Aerosol
French National Institute for Industrial Environment and Risks (Ineris) - CHIMERE Workshop 2026
Fossil Fuel Sources
Biomass Burning Sources
Wood burning
(Wildfires)
POA Primary Organic Aerosol
Particle Emissions
Particle Emissions
BVOC
Biogenic Sources
Vapor Emissions
Vapor Emissions
SOA Secondary Organic Aerosol
VOC
VOC
Vapor Emissions
Oxidation
(OH, O3, NO3)

## Slide 3
French National Institute for Industrial Environment and Risks (Ineris) - CHIMERE Workshop 2026
PMF: Positive Matrix Factorization
→ method used to quantify sources contributions to OA from ACSM measurements
HOA: Hydrocarbon-like organic aerosol
minimally oxidized or not oxidized → Fossil fuel POA
BBOA: Biomass burning organic aerosol
corelated with the levoglucosan signal→ Biomass burning POA
OOA: Oxygenated organic aerosol
highly oxidized → SOA
Modeling PMF : the results from RI-URBANS
Comparison of diurnal profiles:
None of the models reproduces the PMF-derived diurnal profiles satisfactorily
The treatment of POA differs among models
BBOA is overestimated in winter, and all models except EMEP predict a morning peak that do not appear in the PMF results
OOA is strongly underestimated, particularly in winter
→ How to explain and reduce the discrepancies ?

## Slide 4
Total OA Measurements (ACSM)
Organic Aerosol
French National Institute for Industrial Environment and Risks (Ineris) - CHIMERE Workshop 2026
Fossil Fuel Sources
Biomass Burning Sources
Wood burning
(Wildfires)
POA HOA
Particle Emissions
Particle Emissions
BVOC
Biogenic Sources
Vapor Emissions
Vapor Emissions
SOA OOA
VOC
VOC
Vapor Emissions
Oxidation
(OH, O3, NO3)
SVOC
SVOC
Emissions
Emissions
POA BBOA
→ Considering Semi-volatility of emitted POA

## Slide 5
French National Institute for Industrial Environment and Risks (Ineris) - CHIMERE Workshop 2026
Considering Semi-Volatile POA
WP7 of CAMAERA Project:
→ 4 CTMs
→ 5 one-year simulations (2019) with classic VBS schemes for Semi-Volatile POA
SIM1: non-volatile POA
SIM2 to 5: semi-volatile POA
≠ distributions (Robinson2007, May2013/Huang2018)
≠ aging (kinetics, volatility decrease, mass increase, NO3 reactivity)
CHIMERE
MATCH
EMEP
DEHM
→ Large differences between non-volatile and semi-volatiles configurations for simulated OA
→ Only minor differences are observed among the semi-volatile POA configurations
Underestimation occurs mainly in winter:
Very low simulated SOA/OOA concentrations, below 1 µg/m3 compared to 4 µg/m3 in ACSM measurements
The underestimation cannot be explained by a lack of POA emissions
Average annual diurnal cycle (total OA)
µg/m3

## Slide 6
Total OA Measurements (ACSM)
Organic Aerosol
French National Institute for Industrial Environment and Risks (Ineris) - CHIMERE Workshop 2026
Fossil Fuel Sources
Biomass Burning Sources
Wood burning
(Wildfires)
POA HOA
BVOC
Biogenic Sources
Vapor Emissions
Vapor Emissions
SOA OOA
VOC
VOC
Vapor Emissions
Oxidation
(OH, O3, NO3)
SVOC
SVOC
Emissions
Emissions
POA BBOA
→ Are we missing large VOC emissions of SOA precursors ?
IVOC
IVOC
Vapor Emissions
Vapor Emissions

## Slide 7
About Intermediate Volatility Organic Compounds (IVOC)
French National Institute for Industrial Environment and Risks (Ineris) - CHIMERE Workshop 2026
Example of Gas Chromatography
In theory, all gaseous compounds (including IVOC) should be included in the NMVOC emissions
IVOC emissions:
IVOC are commenly associated with the Unresolved Complex Mixture (UCM) observed in gas chromatography. UCM is due to the great number of compounds with many carbons (combination of millions of signal peaks). As the UCM correspond to heavy compounds, UCM should correspond to less volatile part of emissions.
A few studies on European passenger cars suggests relatively low amount of IVOC from european passenger cars (<10% of road-transport NMVOC emissions)
Residential Wood Burning: Very large IVOC emissions have been reported by several studies with IVOC/POA (including condensables) ratio between 2 and 5
Sinha et al. (2023)

## Slide 8
Considering IVOC from FF and BB sources (CAMAERA WP8)
French National Institute for Industrial Environment and Risks (Ineris) - CHIMERE Workshop 2026
Average winter diurnal cycle
total OA (µg/m3)
Use of the standard VBS approach proposed by Ciarelli et al. (2017) based on chamber studies on oxidation of wood burning emissions by OH: IVOC/POA ratio of 4.75 for BB
VBS with IVOC/NMVOC ratio of 0.1 for FF
→ Only limited changes…
→ Are key IVOC and SVOC oxidation pathways missing from the model?
→ More complex mechanisms are needed to answer
→ Are model species being assigned correctly to PMF factors?
POA HOA
POA BBOA
SOA OOA
?
?
?

## Slide 9
French National Institute for Industrial Environment and Risks (Ineris) - CHIMERE Workshop 2026
Development of a complex deterministic mechanisms for FF OA
For simulations with CHIMERE-SSHaerosol
Emission distribution based on May et al. (2013) Work
Explicit molecular structures used to calculate properties (non-ideality, solubility, …)
Chemistry based on SAR from GECKO-A and MCM mechanisms
OH chemistry representing functionalization, fragmentation or function modification
RO2 chemistry representing effect of NOx regime or autoxidation on added functions and loss of volatility
Possibility to represent IVOCs
Adjustable HOA and OOA separation
Added functions per ox. Step:
+ 47% nitrate
+ 48% alcohol
+ 71% ketone
+ 3% hydroper.
Fossil Fuel semi-volatile POA
Volatility nb. | Structure (linear alkane) | LOG(Psat) (atm) | Mw
1 | C10 | -3 | 142
2 | C15 | -5 | 212
3 | C20 | -7 | 282
4 | C25 | -9 | 352
5 | C30 | -11 | 422
nV | C35 | -13 | 492
(-5 /ox. Step)
(-20 /ox. Step)

## Slide 10
French National Institute for Industrial Environment and Risks (Ineris) - CHIMERE Workshop 2026
Development of a complex deterministic mechanisms for BB OA
Species | Psat (atm)
Ph1 | 3,2 × 10-6
Ph2 | 3,2 × 10-8
Alkoic | 10-8
Levo | 2,5 × 10-9
Res | 10-11
Sugar | 10-13
Complex mixture of chemically diverse compounds: molecular approach
Speciation based on Schauer et al. (2001) and Hatch et al. (2018)
Distribution based on May et al. (2013) and Hatch et al. (2018)
Oxidation based on SAR from GECKO-A, simplified (RO2 chemistry, etc.)
BBOA and OOA adjustable separation (BBOA only linked to levoglucosan/sugar?)
→ Ph1 is IVOC
→ Phenols Ph1 and Ph2 can react rapidly and across multiple oxidation steps with NO3.
→ Levoglusosan oxidation produces more volatile compounds
Biomass Burning semi-volatile POA

## Slide 11
Lastest IVOC test results
French National Institute for Industrial Environment and Risks (Ineris) - CHIMERE Workshop 2026
Total OA (µg/m3)
Hour of the day
→ Strong concentrations increase are observed at night while concentrations remain too low during daytime.
Ph1
Ph1N
Ph1NN
+ NO3
+ NO3
→NO3 driven IVOC chemistry could explain a large fraction of the discrepancy between simulations measurements
Average winter diurnal cycle
Hypothesis: Phenolic compounds = 30% IVOC
(10-30% found in experimental studies)
Night-time chemistry could be important. Part of compounds could be phenolic compounds with high reactivity
with the NO3 radical
  Oxidation by OH lifetime around a few days in winter
  Oxidation by NO3 lifetime around 1h in winter

## Slide 12
→ Observed OOA concentrations can be reproduced when phenolic compounds are included
French National Institute for Industrial Environment and Risks (Ineris) - CHIMERE Workshop 2026
Total OA (µg/m3)
Average winter diurnal cycle
Green: Addition of IVOC representing phenolic and non-phenolic (using the mechanism for alkanes) compounds
Red: All IVOC compounds are represented using the alkanes oxidation mechanism
→ The model-measurment gap can largely be closed
OOA (µg/m3)
Last IVOC test results

## Slide 13
Conclusions and perspectives
French National Institute for Industrial Environment and Risks (Ineris) - CHIMERE Workshop 2026
Missing phenolic IVOCs and their NO₃ chemistry may explain a large part of the winter organic aerosol underestimation in CHIMERE
Standard semi-volatile POA treatments do not increase simulated OA and do not explain the winter OOA deficit.
Adding IVOC emissions using standard VBS approaches leads to only limited improvements.
Deterministic molecular mechanisms highlight the importance of phenolic IVOCs emitted by residential wood burning.
Night-time oxidation by NO₃ radicals appears to be a key pathway for winter SOA formation.
Including phenolic IVOCs substantially improves agreement with ACSM measurements and PMF-derived OOA.
Perspectives
Improve European IVOC emission inventories, especially for residential wood combustion.
Better constrain IVOC composition and volatility distributions using laboratory and field measurements.
Consider new sources for OA: Volatile Chemical Products IVOC (solvents) or Cooking emissions
Refine the mapping between model species and PMF factors (HOA, BBOA and OOA).

## Slide 14
Conclusions and perspectives
French National Institute for Industrial Environment and Risks (Ineris) - CHIMERE Workshop 2026

## Slide 15
Phenol mechanism
French National Institute for Industrial Environment and Risks (Ineris) - CHIMERE Workshop 2026
Ph
[ ]
×0,5
x
-2
-4
-6
-8
Log(Psat)
Log(Heff)
x
+5
+10
PhN
PhO
PhNN
PhON
PhOO
PhONN
PhOON
PhOOO
PhBpnV
Phopen
+ OH
+ NO3
Pour Ph1 uniquement
→ Ph1 et Ph2
Inclut la chimie radicalaire
N: ajout fonction nitrite
O: ajout fonction alcool
[-NO2/=O/-OH/-OOH]
Ph1open:
[-NO2/-OH/-OOH]
Ph1BpnV:

## Slide 16
Resine mechanism
French National Institute for Industrial Environment and Risks (Ineris) - CHIMERE Workshop 2026
Res
→ Sugar : non-volatil
→ Alkoic : vieillissement similaire aux POA du trafic
→ Res :
RO2
Resopen
ResnV:
+ OH
+ NO3
+ O3
+ NO / HO2
C20 avec:
1 double liaison
0.43 alcool
1 cétone
0.74 aldéhyde
1 acide
0.97 nitrate
0.27 hydroperoxyde

## Slide 17
Levoglucosan mechanism
French National Institute for Industrial Environment and Risks (Ineris) - CHIMERE Workshop 2026
→ Levo :
RO2
+ NO / HO2
RO2
+ HO2
+ NO
RO2
+ NO2 / HO2
RO2
+ NO2 / HO2
+ NO
[-OONO2/-OOH/-OH]
[ ]
+ OH
+ NO3
[ONO2/OH/OOH]